## Slide 1
MICRO-DOPPLER
SPECTROGRAM CLASSIFIER
CNN-Based Target Classification from Radar Signatures
Humans • Vehicles • Drones • Animals

## Slide 2
PIPELINE OVERVIEW
Synthetic Data
Simulate IQ returns →
STFT spectrograms
01
Dataset & Loader
Package spectrograms
+ labels for PyTorch
02
2D CNN Model
Convolutional feature
extraction on images
03
Train & Validate
Adam optimizer,
LR scheduling
04
Evaluate
Confusion matrix,
ROC curves
05

## Slide 3
TARGET CLASSES
Humans
Periodic limb-swing gait
signatures (~1-3 Hz)
Vehicles
Strong bulk Doppler,
minimal micro-Doppler
Drones
High-frequency rotor
blade flashes (50-200 Hz)
Animals
Irregular, lower-frequency
motion patterns

## Slide 4
CNN ARCHITECTURE
356,164 total parameters
Feature Extraction
Conv2d(1→32, 3×3)
BatchNorm2d + ReLU
MaxPool2d(2)
Conv2d(32→64, 3×3)
BatchNorm2d + ReLU
MaxPool2d(2)
Conv2d(64→128, 3×3)
BatchNorm2d + ReLU
AdaptiveAvgPool2d(4×4)
Classifier
Flatten
Linear(2048→128)
BatchNorm1d + ReLU
Dropout(0.5)
Linear(128→4)

## Slide 5
TRAINING DETAILS
Total Samples
2,400
600 per class
Data Split
70/15/15
Train / Val / Test
Batch Size
32
Efficient processing
Optimizer
Adam
LR: 0.001
Early Stop
Epoch 29
Best val loss: 0.0003
Test Accuracy
100%
All classes separated

## Slide 6
MICRO-DOPPLER SIGNATURES
Humans
Periodic limb-swing patterns are highly distinctive; sinusoidal gait cadence at 1-3 Hz.
Vehicles
Strong constant Doppler separates them clearly; engine vibration at 20-60 Hz with high bulk velocity.
Drones
High-frequency rotor harmonics (50-200 Hz) provide a unique fingerprint across multiple harmonics.
Animals
Irregular, bursty motion is the hardest to separate from humans; random walk Doppler patterns.

## Slide 7
CONCLUSION & NEXT STEPS
Achieved high classification accuracy across all four target classes
Synthetic STFT spectrograms effectively simulate micro-Doppler signatures
2D CNN with 356K parameters converges by epoch 29 with early stopping
NEXT STEPS
1. Replace synthetic data with real micro-Doppler recordings
2. Add data augmentation (time-shift, frequency jitter, SNR variation)
3. Experiment with ResNet / EfficientNet backbones
4. Integrate with presence heatmap for end-to-end pipeline