## Slide 1
PRESENCE HEATMAP
GENERATOR
Spatial Density Mapping from Fused Radar & Cell Data
2 km × 2 km Surveillance Area • 5,000 Detections • 4 Cell Towers

## Slide 2
PIPELINE OVERVIEW
Radar
Detections
Simulate time-stamped
target pings (x, y)
01
Cell-Sector
Data
Model tower sectors
with coverage
02
Data
Fusion
Merge radar & cell
observations
03
Heatmap
Generation
Spatial density
maps
04
Temporal
Analysis
Compare across
time windows
05

## Slide 3
SIMULATION PARAMETERS
Surveillance Area
2 km²
2000m × 2000m grid
Grid Resolution
20m
100 × 100 cells
Time Window
1 Hour
08:00 → 09:00
Radar Detections
5,000
Clustered at hotspots
Cell Towers
4
3 sectors each (12 total)
Smoothing
σ = 2.5
Gaussian filter

## Slide 4
DATA FUSION APPROACH
Radar Detections
Time-stamped (x, y) coordinates
Detection confidence scores (0-1)
Clustered around 5 hotspot areas
Cell-Sector Data
Directional angular coverage
Signal strength (inverse-square decay)
Baseline weight 0.3 outside sectors
Fusion Formula
fused_score = radar_confidence × cell_signal_strength

## Slide 5
KEY FINDINGS
4.58
Peak Density
Score
0.499
Mean Fused
Score
0.990
Max Fused
Score
Fused vs Radar-Only
The fused heatmap sharpens hotspot contrast compared to radar-only density maps.
Cell Weighting Effect
Cell-sector weighting suppresses low-confidence detections far from towers.
Temporal Patterns
15-minute time slicing reveals how movement concentration shifts over the hour.

## Slide 6
CONCLUSION & NEXT STEPS
Successfully fused 5,000 radar detections with 12 cell sectors
Spatial density grid: 100×100 cells covering 2 km × 2 km area
Fused heatmap sharpens hotspot detection vs radar-only approach
NEXT STEPS
1. Replace synthetic data with real radar tracks & CDR logs
2. Bayesian or Kalman-filter fusion for multi-source weighting
3. Add class-specific heatmap layers (humans, vehicles, drones)
4. Stream radar detections in real time with rolling updates
5. Export density maps as GeoTIFF for GIS overlay